## Slide 1
01 · LITERATURE
What existing PCB defect detection papers have already solved
Research gap & novelty · 1
ALREADY ACHIEVED
High mAP@0.5
≈97–99.5 % on public benchmarks [1]
YOLO-based real-time detection
Single-stage detectors dominate [1][2][4]
Feature fusion for small defects
Dynamic multi-scale fusion, P2 heads [1]
Long-tail class imbalance
Adaptive tail attention [1]
Lightweight model design
8.61 M params [1]; INT8 / mixed quantization [2][4]
Edge-device deployment
Jetson Orin NX [1]; PYNQ-Z2 FPGA [2][4]
Example: LDM-PCB [1] long-tail · multi-scale · fine-grained feature loss
Adaptive tail attention + dynamic multi-scale fusion + high-resolution prediction layer
99.1 %
mAP@0.5
81.6 %
mAP@0.5:0.95
8.61 M
parameters
100
FPS (RTX 3090 Ti)
Self-built 940-image soldering dataset; ≈10 FPS on Jetson Orin NX
[2] YOLOx-Plus + FPGA
Attention + SIoU; INT8/INT16 mixed quantization on PYNQ-Z2
90.1 % mAP · 72.6 FPS
[3] FPGA image processing
Binary golden-reference XOR comparison in Verilog, 1024×1024
No training data; simulation only
[4] YOLOv8n on PYNQ-Z2
INT8 + pruning; FPGA fabric runs the convolutions
P / R 98.5 % · 0.15 s inference
Takeaway: accuracy on public benchmarks is largely solved — the open questions are elsewhere.
[1] Li et al., Eng. Appl. Artif. Intell. 165 (2026) 113415 [2] Pan et al., IEEE Access 12 (2024) 61343 [3] Navaneeth & Kannan, ICCPCT 2025 [4] Sagayaraj et al., ICDCS 2026
Notes: Accuracy on public / controlled benchmarks is largely solved. LDM-PCB numbers are on its self-built 5-class soldering-defect dataset with an RTX 3090 Ti; on Jetson Orin NX the same model runs at about 10 FPS.

## Slide 2
02 · RESEARCH GAP
What existing papers still cannot fully solve
Research gap & novelty · 2
Aspect | Existing works | Research gap | My proposed solution
Scope | Mainly new detector architectures [1][2] | Full hardware–software inspection pipeline rarely evaluated | FPGA preprocessing + YOLO evaluated as one chain
Data | Public or self-built controlled datasets, random splits [1][2] | Industrial generalization still uncertain | Group-aware split now; company PCB images next
Metric | mAP@0.5 ≈ 99–99.5 % for most YOLO models [1] | Strict localization (mAP@0.5:0.95) remains harder | mAP@0.5:0.95 + per-class AP as primary metrics
Features | Attention and multi-scale fusion learn cues implicitly [1][2] | Explicit structural edge cues rarely used | Defect-oriented edge enhancement
Pre-processing | Resize / filter / normalize in software [1][4] | Software preprocessing adds latency on every image | Move deterministic filtering to FPGA
Deployment | FPGA accelerates the CNN itself [2][4] | Resources, interface overhead, end-to-end FPS not deeply measured | Report LEs, memory, transfer time, end-to-end FPS
Trade-off | Accuracy first, speed second [1] | Accuracy–latency–resource trade-off not analysed jointly | Full trade-off evaluation
Gap in one line: no reviewed study measures whether hardware edge preprocessing helps a lightweight YOLO in accuracy and in end-to-end latency and FPGA resources together.
[1] Li et al., Eng. Appl. Artif. Intell. 165 (2026) 113415 [2] Pan et al., IEEE Access 12 (2024) 61343 [3] Navaneeth & Kannan, ICCPCT 2025 [4] Sagayaraj et al., ICDCS 2026
Notes: Table reads left to right: what the literature does, what is still missing, and how my work responds. Evidence numbers are taken from refs [1]–[4].

## Slide 3
03 · MY RESEARCH
What my research tries to solve
Research gap & novelty · 3
Not another YOLO model — a hardware–AI co-design study
FPGA · Cyclone IV E
HOST · GPU / edge-AI
Original PCB image
Sobel / edge enhancement
Edge-enhanced image fusion
Lightweight YOLO
Real-time defect decision
1
Use edge information for topology-sensitive defects
2
Move deterministic preprocessing from software to FPGA
3
Compare original vs edge-enhanced YOLO fairly
4
Measure latency, FPS, FPGA resources and end-to-end performance
5
Find which defect classes benefit from edge enhancement
6
Judge practicality for low-cost AOI deployment
Notes: Emphasise: this is not another YOLO architecture. It is a hardware–AI co-design study with a fair, fully measured comparison.

## Slide 4
04 · NOVELTY AND LIMITATION
Novelty of my work — and its honest limits
Research gap & novelty · 4
NOVELTY
1
Defect-oriented edge enhancement
Targets trace breaks, abnormal connections, extra copper, hole boundaries
2
FPGA-assisted preprocessing
Hardware filtering instead of software-only preprocessing
3
Hardware–AI co-design
FPGA edge extraction + lightweight YOLO detector
4
Full trade-off evaluation
P, R, F1, mAP@0.5, mAP@0.5:0.95, per-class AP, latency, FPS, FPGA resources
5
Fair baseline comparison
Baseline vs edge-enhanced YOLO: same split, same protocol
LIMITATIONS
Public PCB images only; company images not yet available
2D RGB only; no 3D depth information
Edge enhancement may not improve every metric (clean split: recall / F1 up, mAP@0.5:0.95 not)
Cyclone IV E: limited memory and interface bandwidth
Notes: Current clean-split evidence (one seed): recall +0.0082, F1 +0.0048, mAP@0.5:0.95 −0.0026. So the novelty must be proven through efficiency and per-class analysis, not assumed.